## Slide 1
Figures of Merit
Flux: photons/sec/0.1% bandwidth/horizontal mrad/mA
  Number of photons per bandwidth per unit time integrated over the entire vertical opening angle ψ.
  Relevant for unfocused beamlines with large samples, or with large collection optics that focus on sample, but focal spot size is not particularly important
  Can be improved by beamline optics (decreasing angle)
Intensity: flux/vertical angle ψ
  Number of photons per bandwidth, per unit time, per unit solid angle.
  Relevant for experiments that use a pinhole or collimator to select a small beam.
  Useful for determining flux that an optical element can collect
  Can be improved by beamline optics (decreasing angles)
Brightness: intensity/source area (mm2)
  Number of photons per bandwidth, per unit time, per unit solid angle, per unit source area.
  Relevant for a beamline with focusing optics where the focal spot size is important, i.e. microprobe or microscope.
  Cannot be improved by beamline optics, brightness is conserved. Optics can change the size or the divergence, but the product is constant

## Slide 2: Intensity of COMPRES sources Figure of merit for beamline without focusing, e.g. slits on LVP

## Slide 3: Intensity of COMPRES sources
NSLS-II damping wiggler (XPD) is about 15X more intense than X-17 at 40keV, same at 100 keV
  NSLS-II beamlines are ~2X longer than X-17, so flux through pinhole will be about 2.5X more: not very different
APS Undulator A is 100-1000x more intense than NSLS-II DW90 (XPD) and NSLS-II SCW (HEX)
APS bending magnet is 100-100x less intense than NSLS-II DW90 (XPD) and NSLS-II SCW (HEX)
APS tapered undulator is ~10X more intense than NSLS-II SCW (HEX) at all energies.
APS-U undulators will be more intense than NSLS-II undulators above 5 keV.
ALS superbend is 5-10x less intense than APS bending magnet

## Slide 4: Brightness of COMPRES sources Figure of merit for beamline with focusing, i.e. diamond anvil cell

## Slide 5: Brightness of COMPRES sources
APS undulator is 10X brighter than NSLS-II DW90 (XPD) APS undulator at 30 keV where much DAC diffraction is done.
NSLS-II SCW (HEX) is similar brightness to APS undulator above 50 keV
ALS superbend is brighter than APS bending magnet below 60 keV because the source is smaller.
APS-U undulators are 15-100x brighter than APS now and 1000x brighter than either NSLS-II DW90 (XPD) or NSLS-II SCW (HEX) at all energies