## Slide 1: COMPRES/GSECARS Gas Loading System Update
COMPRES Annual Meeting
July 10, 2017

## Slide 2: COMPRES/GSECARS Gas Loading Facility
System in operation for nearly 9 years
Has had a major impact on how diamond anvil cell experiments are done at synchrotrons.
Prior to 2008 very few cells were loaded with Ne or He.
  Mostly limited to users from Carnegie or Livermore.
Now the majority of x-ray measurements are done with gas loading.
  Significant improvement in data quality.
COMPRES supported initial capital equipment costs and 50% of Sergey Tkachev to provide mail-in service and loading for non-GSECARS users
GSECARS designed and constructed system, and pays operations costs

## Slide 3: COMPRES/GSECARS Gas Loading
.
 | Users per year | Unique users per year | Loadings per year
2010 | 149 | 55 | 206
2011 | 288 | 86 | 420
2012 | 361 | 109 | 516
2013 | 403 | 145 | 646
2014 | 360 | 156 | 562
2015 | 531 | 163 | 738
2016 | 549 | 195 | 747
2017 (to 7/7) | 397 | 90 | 489
Total | 3038 | 999 | 4324
Systems built and delivered by University of Chicago Engineering Center: CalTech
ALS (Lawrence Berkeley National Laboratory)
Sandia National Laboratory
Brazilian Synchrotron Light Laboratory

## Slide 4: Last Year: The Neon Price Crisis
The price of neon increased by a factor of 7 in 2015-16
  Standard 6,000 liter cylinder increased from ~$3,000 to ~$22,000.
    We use about 3 cylinders/year, so cost would have risen to $66,000 which is not affordable
Solutions:
  Purchase from Ukrainian supplier: 2 cylinders for ~$3,700 each. Even with air freight, customs, and delivery from O’Hare we save $48K compared to purchasing from the US supplier, or a factor of 7 less.
  New low-pressure compressor with a minimum inlet pressure of 50 PSI, purchased by COMPRES for $9,000.
    Allows using the last 500 PSI in the large gas cylinder (~25%)
    Allows recovering nearly all of the gas from the pressure vessel back into the lecture bottle

## Slide 5: This Year: Xenon and Krypton
We have not been able to supply xenon to users in the past because:
  Price from the U.S. supplier is $50/liter, which is 100X more expensive than neon.
  We were not able to recover most of the xenon from the pressure vessel
Same solutions as neon:
  Purchase from Ukrainian supplier: Price is $12/liter, or 4X less.
  New low-pressure compressor lets us recover most of the gas from the pressure vessel back into the lecture bottle.
We now offer xenon loading to users who request it.
Krypton is reasonably priced, and we now offer that as well.

## Slide 6: Publications Acknowledging COMPRES/GSECARS Gas Loading System in APS Publication Database
.
Year | Publications
2008-2010 | 6
2011 | 7
2012 | 19
2013 | 23
2014 | 24
2015 | 43
2016 | 39
2017 (to 7/7) | 18
Total | 179
These statistics are certainly under-reported. Everyone who uses the gas loading system should acknowledge it in their papers and inform Nancy Lazarz at GSECARS who will enter it in the APS publication database. Information at:
http://gsecars.uchicago.edu/page/gsecars-publications
These credits help both COMPRES and GSECARS with our funding agencies.