## Slide 1: US Facilities for Diamond Anvil Cell Research
COMPRES Workshop
October 28, 2017

## Slide 2: Outline
Comparison of source properties at the different synchrotrons
Overview of existing “dedicated” beamlines for diamond cell research in the US
My thoughts on what a proposal for DAC at NSLS-II will need

## Slide 3: Synchrotron Sources for DAC Beamlines
Past sources | 
NSLS X-17 SCW | NSLS-X17 superconducting wiggler
Current sources | 
ALS SB | ALS superbend beamline 12.2.2
APS BM | APS bending magnet
APS UA | APS 33mm period undulator untapered
APS UA | APS 33 mm period undulator tapered
NSLS-II U20 | NSLS-II 20mm period undulator at HXN
NSLS-II DW90 | NSLS-II 90 mm period damping wiggler at XPD
Potential future sources | 
NSLS-II SCW 4T | NSLS-II 4 tesla superconducting wiggler at HEX
APS-U U27.5 | APS upgrade 27.5 mm period normal undulator
APS-U SCU18 | APS upgrade 18 mm period superconducting undulator
APS-U TPW | APS upgrade three pole wiggler

## Slide 4: Intensity of DAC sources Figure of merit for beamline without focusing, e.g. slits on LVP

## Slide 5: Brightness of DAC sources Figure of merit for beamline with focusing, i.e. diamond anvil cell

## Slide 6: Brightness of DAC sources
APS undulator is 10X brighter than NSLS-II DW90 (XPD) APS undulator at 30 keV where much DAC diffraction is done.
NSLS-II SCW (HEX) is similar brightness to APS undulator above 50 keV
ALS superbend is brighter than APS bending magnet below 60 keV because the source is smaller.
APS-U undulators are 15-100x brighter than APS now and 1000x brighter than either NSLS-II DW90 (XPD) or NSLS-II SCW (HEX) at all energies

## Slide 7: Beamline 12.2.2 at the Advanced Light Source
Superconducting bending magnet source
Approved Program with COMPRES guarantees 35% of beam time.
  In practice >50%.
  One other approved program HPSTAR has 15%
  COMPRES proposals generally do well in General User program
COMPRES contributes 2 beamline scientists, Christine Beavers and Jinyuan Yan.
Technical specialties
  Radial diffraction with external and laser heating
  Single-crystal diffraction (still developing)

## Slide 8: Beamline 12.2.2
Endstation 1 (ES1)
Endstation 2 (ES2)

## Slide 9: Endstation 2- High Pressure
10x10 mm2 X-ray spot
10-35keV
Axial & Radial Geometries
Shutterless Single Crystal
Laser Heating
  Pyrometry and Peak Scaling method implemented.

## Slide 10: Beamlines 3-ID and 30-ID at the Advanced Photon Source
Undulator sources
  2x22.7 cm and 2x1.7cm period, optimized
COMPRES contributes 75% of beamline scientist, Wenli Bi.
No guaranteed beam time, but COMPRES users are successful in General User program
  ~40% of time to COMPRES community
Technical specialties
  Nuclear Resonance Inelastic Scattering (NRIXS)
  Synchrotron Mossbauer Spectroscopy (SMS)
  High Energy Resolution Inelastic Scattering (HERIX)

## Slide 13: HPCAT Sector 16 at the Advanced Photon Source
2 undulator beamlines, 2 bending magnet beamlines
100% of time for high-pressure
  DAC and Paris-Edinburgh cell
Major funding from NNSA with 75% of time to NNSA funded investigators
  25% of time for General Users
  COMPRES community typically 15%-20% of each beamline

## Slide 14: HPCAT – Four Beamlines
Sector 16
Canted undulator beams
ID-C/D/E:
Spectroscopy
Scattering
XES,IXS – 1eV
NRIXS – 2meV
IDB:
Micro-diffraction
(high photon flux)
Laser heating (>3000K)
Cryostat (<4k)
Sector 16
Bending magnet beam
BMB:
White Laue
Paris-Edinburgh
Press
(fast x-ray imaging)
BM-C/D:
Micro-diffraction
XANES
Split in space
14-42 keV
5-36 keV

## Slide 15: GSECARS Sector 13 at the Advanced Photon Source
2 undulator beamlines, 2 bending magnet beamlines
Funding from NSF-EAR with 100% of time available to geoscience community through General User program
13-ID-D
  Double sided laser heating (pulsed), emission spectroscopy, fast Pilatus 3X CdTe detector
  ~60% time
13-BM-D
  Brillouin scattering with online x-ray diffraction, external heating
  ~50% time
13-BM-C (PX^2 partnership with COMPRES)
  Single crystal diffraction in DAC, external and laser heating
  ~75% time

## Slide 16
X-ray energy 5-80 keV
beam size ~3 µm
XRD, sXRD, XES
on-line laser heating,
Raman and
VIS-IR spectroscopy
Five optical focal points (x-ray, lasers, spectroscopy)
are aligned with precision better than 1 µm in the DAC
X-ray energy 5-80 keV
beam size ~6 x 12 µm
XRD, sXRD
on-line Brillouin, Raman
VIS-IR spectroscopy
X-ray energy 15, 28.6 keV
beam size ~ 15 µm
sXRD
on-line laser heating, Raman and
VIS spectroscopy
13-IDD
13-BMD
13-BMC
Notes: To utilize different approaches for sample characterization we have built three dedicated stations: main IDD combined with LH and on-line advanced optical spectroscopy, BMD coupled with BS, and BMC for sXRD where 6-axis diffractometer is combined with LH, Ruby and Raman

## Slide 17
Gas-loading system
Raman system
Preparation lab
Laser heating/cutting
Cryogenic loading
Micro-manipulator
Supporting equipment
Notes: Significant infrastructure development is required to maintain DAC program

## Slide 18
High pressure single crystal diffraction setup at 13-BM-C
Diffraction peaks rendered with ATREX/RSV software package
Crystal structure of omphacite resolved at high pressure
PX^2: high pressure meets single crystal diffraction
Pressure-volume equation of state of omphacite and elasticity
Diffraction image
Partnership for eXtreme Xtallography (PX^2) is supported by:
Zhang, Hu and Dera, under review

## Slide 19
X-ray
beam
Sample rotation
Fast high pressure single crystal measurements
+/-33 degrees, 0.5” step, 0.2s exposure, 133 files => 27s
Wide scan
Step scan
File | STX.CurrentPosition | STX.FollowingError | STX.SetpointPosition | STX.CurrentVelocity | STZ.CurrentPosition | STZ.FollowingError | STZ.SetpointPosition | STZ.CurrentVelocity | STY.CurrentPosition | STY.FollowingError | STY.SetpointPosition | STY.CurrentVelocity | OM.CurrentPosition | OM.FollowingError | OM.SetpointPosition | OM.CurrentVelocity | 
enst_s1_001 | 1.2783 | 0 | 1.2783 | 0 | 3.3528 | 0 | 3.3528 | 0 | -2.1040404 | 0 | -2.1040404 | 0 | -123.001 | 0.001 | -122.9997996 | 0.354583658 | 
enst_s1_001 | 1.2783 | 0 | 1.2783 | 0 | 3.3528 | 0 | 3.3528 | 0 | -2.1040404 | 0 | -2.1040404 | 0 | -122.9 | 0 | -122.8998 | 0.408675801 | 
enst_s1_001 | 1.2783 | 0 | 1.2783 | 0 | 3.3528 | 0 | 3.3528 | 0 | -2.1040404 | 0 | -2.1040404 | 0 | -122.8005 | 0.0005 | -122.7998 | 0.58559678 | 
enst_s1_001 | 1.2783 | 0 | 1.2783 | 0 | 3.3528 | 0 | 3.3528 | 0 | -2.1040404 | 0 | -2.1040404 | 0 | -122.7 | 0 | -122.6998 | 0.696227079 | 
enst_s1_001 | 1.2783 | 0 | 1.2783 | 0 | 3.3528 | 0 | 3.3528 | 0 | -2.1040404 | 0 | -2.1040404 | 0 | -122.6 | 0 | -122.5998 | 0.484909907 | 
Log file from Newport XPS

## Slide 20
Sample
X-ray beam
Detector
MC
Comparison between measurements of Mg2SiO4 sample in a Diamond Anvil Cell with and without Multichannel Collimator (MCS).
Multichannel Collimator
The upstream block is composed of 75 slits of 50 µm positioned at a distance of 50 mm from the sample. The downstream block is composed of 75 slits of 200 µm positioned at 200 mm
Notes: One of the central aspects for obtaining high quality structural information of disordered materials by X-ray diffraction is perfect background subtraction. This is particularly difficult when employing high-pressure vessels, such as diamond anvil cells (DAC) and Paris-Edinburgh large volume presses (PEP). Their background contribution is very high compared to the low diffuse scattering signal of the sample, especially at high diffraction angles, and furthermore the background is changing during compression and decompression.
In order to overcome this challenge we have successfully installed a multichannel collimator (MCC) for the DAC setup at the GSECARS 13-IDD beamline, APS

## Slide 21: Summary of US DAC Beamlines
Beamline | % of time for COMPRES DAC | Laser heating | Specialty Techniques
ALS 12.2.2 | 60% | Yes | Radial diffraction; single-crystal
APS 3-ID | 40% | Yes | NRIXS, SMS, HERIX
APS 16-ID-B | 20% | Yes | Cryostats, time-resolved
APS 16-ID-D | 15% | No | NRIXS, SMS, emission spectroscopy
APS 16-BM-B | 15% | No | Laue diffraction, PE cell
APS 16-BM-D | 20% | No | XANES
APS 13-BM-D | 50% | No | Brillouin
APS 13-BM-C | 75% | In commissioning | Single crystal
APS 13-ID-D | 60% | Yes | Pulsed heating, emission spectroscopy
TOTAL | 355% |  | 

## Slide 22: Questions for NSLS-II DAC Proposal
What would be the specialty techniques at XPD?
Would it include online laser heating?
  Who would be in charge of getting it working?
  Is laser heating equipment from X17-B3 available for use at NSLS-II?
Who are the major potential users of the facility?
  Important to identify a core set of users who view the NSLS-II facility as critical to their research.
  Need to be members of the COMPRES community, i.e. users from US whose research is focused on earth science problems.
What is the management plan?
  Who will be local to the NSLS-II to keep the project on track?
  Who will provide the scientific driving force?

## Slide 23: Questions for NSLS-II DAC Proposal
What capital equipment expenditures will be required to produce a competitive DAC station?
  Micro-focusing optics
  Detectors
  Laser heating
  Sample manipulation
  Equipment for specialty techniques
What fraction of time can COMPRES DAC users be guaranteed
  What is the maximum amount of time they might realistically be expected to receive if they write excellent General User Proposals?